Pulse rain sensor user's Guide

JXBS-3001-MCYL

Ver1.0

# Chapter 1 Product Introduction

## 1.1 Product overview

The JXBS-3001-YL series rain sensor is an instrument that can automatically observe and store "rainfall" parameters. It is divided into two types: ABS and stainless steel.

The sensor developed by our company is small and light, easy to carry and assemble. It is used to measure the rainfall in nature and convert the rainfall into digital information output in the form of switch to meet the needs of information transmission, processing, recording, etc. .

It is widely used in relevant departments such as meteorological stations (stations), hydrological stations, agriculture and forestry, national defense, field observation and reporting stations, and can provide original data for flood control, water supply dispatching, and water regime management of power stations and reservoirs.

## 1.2 Product features

(1) High precision: using electronic circuits and microcomputer technology, the output pulse fertilizer resolution is 0.2mm, and each output pulse represents 0.2mm of rainfall.

(2) The maximum allowable measurement range of rain intensity: the sensor rain intensity measurement range is 0.1mm-3mm/min, up to 5mm/min.

(3) Minimum measurement error: The national standard for rain gauge error is ±4%, but our sensor is developed and produced in accordance with International Meteorological Organization standards, and the error is less than ±3%.

## 1.3 Product advantages

(1) Low cost, strong practicability, and long-term use in the field.

(2) Small size, simple operation and reliable performance.

(3) Made of ABS engineering plastics, no rust.

(4) The water receiving port is made of ABS plastic injection molding and aluminum alloy material, with high smoothness and small errors caused by stagnant water.

(5) The internal tipping bucket is well-manufactured, and the frictional resistance generated is small, so the response is sensitive and the error is small.

(6) The internal chassis is equipped with level adjustment bubbles, which can assist the bottom corner to adjust the equipment to the best level.

(7) The bottom is fixed with iron sheets and expansion screws to ensure stable product performance and reliable work.

## 1.4The main parameters

| parameter | Technical index |
| --- | --- |
| Measuring range | 0.01mm～3mm/min |
| Resolution | 0.2mm |
| Precision | 0.2mm |
| Measurement error | ±3% |
| Response time | Less than 1 second |
| communication method | Pulse type |
| Baud rate | 2400/4800/9600 |
| Power supply mode | 12V-24V DC |
| Power consumption | <1W |
| Working temperature environment | -10-50℃ |
| Working humidity environment | 0-95% (relative humidity), no condensation |
| Water-bearing caliber | ABS material：164mm |
|  | aluminum alloy：200mm |
| Appearance material | ABS material |
|  | aluminum alloy |

# Chapter 2 Hardware Connection

## 2.1 Inspection before equipment installation

Please check the equipment list before installing the equipment:

| name | Quantity |
| --- | --- |
| High precision sensor | 1set |
| 12V waterproof power supply | 1set（选配） |
| Expansion screw | 4 |
| Iron sheets | 2 |
| Nut screw | 4 |
| Warranty card/certificate | 1 serving |

## 2.2 Product appearance size and internal structure

### 2.2.1 Appearance size

The following figure is the appearance and size of the sensor, which can be installed reasonably according to the size, as shown in the figure:

### 2.2.2 Internal structure

The following figure shows the internal structure of the product, as shown in the figure:

## 2.3 Interface description

The power interface is a wide-voltage power input of 12-24V. The wiring of the pulse signal line is yellow, and the line sequence description is shown in the following figure (table):

|  | Thread color | Description |
| --- | --- | --- |
| power supply | brown | Power is positive（12-24VDC） |
|  | black | Power negative |
| Communication | yellow | Pulse signal line |

Note: There is no yellow line in the line sequence that may be provided in some factory batches. At this time, the gray line is equivalent to replace the yellow line.

## 2.4Installation instructions

(1) First use the screws delivered by our company to fix the patch on the bottom of the sensor, and at the same time install the expansion screw at the corresponding position of the iron sheet.

(2) Determine the installation position, and then drill or install according to the distance between the expansion screws at the bottom of the sensor.

(3) Fix the sensor to the position to be installed, and observe the horizontal bubble (yellow) to maintain the middle position; keep the sensor at the best level to ensure the accuracy of the rainfall data.

(4) Before the sensor is shipped, the internal tipping bucket should be bound with a cable tie, and the strapping should be cut off before use.

(5) After the above steps are completed, the device can work after power on.

2.5 Notes

(1) Please check whether the packaging is intact, and check whether the transmitter model and specifications are consistent with the product you have purchased; if you have any questions, please contact our after-sales company as soon as possible.

(2) Before using the sensor, please read the product manual in detail or consult our after-sales staff.

(3) Confirm whether the output voltage of the power supply is correct, and whether the positive and negative wiring of the power supply and the positive and negative wiring of the product are consistent with the manual. Incorrect wiring will cause the equipment to burn.

(4) The equipment must be fixed with expansion screws delivered by our company or corresponding to the size.

# Chapter 3  Appendix

## 3.1 Warranty and after-sales

The warranty clauses follow the sensor after-sales clauses of Weihai Jingxun Changtong Electronic Technology Co., Ltd., the sensor host circuit part is guaranteed for two years, the gas-sensitive probe is guaranteed for one year, and the accessories (shell/plug/cable, etc.) are guaranteed for three months.

Chapter 4 Configure software installation and use

4.1

When the sensor is connected to the computer through the USB to 485 correctly and provides power, you can see the correct COM port in the computer (see the COM port in my computer-property-device manager-port).

As shown above, your serial number is COM10, remember this serial port, you need to fill in the sensor monitoring software.

If no COM port is found in the device manager, it means that you did not insert USB turn 485 or install the driver correctly. Please contact the technician for help.

4.2  Use of sensor monitoring software

The software interface is shown in the figure:

After opening the software, first select the "sensor type" at the top of the software, then get the serial port number and select the correct serial port according to the method of Chapter 3.1. Then click Auto get current baud rate and address to automatically detect all devices and baud rates on the current 485 bus. Note that there is only one sensor on the 485 bus when using software automatic acquisition. Then click connect device to get sensor data information in real time.

4.3 Modifying baud rate and device address

In the case of disconnecting the device connection, click "modify baud rate and modify slave station number" in "configure sensor communication parameters" to complete the relevant settings. Please restart the device after setting up. Then automatically get the current baud rate and address find that the address and baud rate have been changed to the address and baud rate you need.

Chapter 5

5.1 Basic communications parameters

| Parameters | Content |
| --- | --- |
| Code | 8-bit binary |
| Data bits | 8 bits |
| parity bit | No |
| Stop position | 1 Position |
| Error calibration | CRC Long loop code |
| baud rate | 2400bps/4800bps/9600 bps can be set, the factory default is 9600bps |

5.2 Data frame format definition

Adopt the Modbus-RTU protocol as follows:

Initial structure >=4 bytes time

Address =1 byte

Function =1 byte

Data =N bytes

Error check =16-bit CRC code

End structure >=4 bytes of time

Address code: the address of the transmitter, unique in the inquiry network (factory default 0 x01).

Function code: the host sends the instruction function prompt, this transmitter only uses the function code 0 x03( reads the memory data).

Data area: data area is a specific query area, note that 16 bits data high byte before

CRC code: two-byte check code.

Question frame

| Address code | Functional code | Register Start Address | Register length | Check the low bit | Check the high bit |
| --- | --- | --- | --- | --- | --- |
| 1byte | 1byte | 2bytes | 2bytes | 1byte | 1byte |

Response frames

| Address code | Functional code | Effective byte | Data area I | Second Data Area | N data area |
| --- | --- | --- | --- | --- | --- |
| 1byte | 1byte | 1byte | 2bytes | 2bytes | 2bytes |

Register address

Examples of communication protocols and explanations

Read the current accumulated rainfall value of the device address 0x01

Question frame

| Address code | Functional code | Starting address | Data length | Check the low bit | Check the high bit |
| --- | --- | --- | --- | --- | --- |
| 0x01 | 0x03 | 0x01,0x05 | 0x00,0x01 | 0x95 | 0xF7 |

Response frames

| Address code | Functional code | Number of valid bytes | Rainfall values | Checking code Low | Checking code High |
| --- | --- | --- | --- | --- | --- |
| 0x01 | 0x03 | 0x02 | 0x00 0x18 | 0xFC | 0x44 |

Rainfall:

0018H( hexadecimal)=24=> rainfall =2.4 mm

Equipment Address 0 x01 Rainfall Clearance Instruction

Question frame

| Address code | Functional code | Starting address | Data length | Check the low bit | Check the high bit |
| --- | --- | --- | --- | --- | --- |
| 0x01 | 0x06 | 0x01,0x08 | 0x00,0x01 | 0xC8 | 0x34 |

Response frames

| Address code | Functional code | Number of valid bytes | Rainfall values | Checking code Low | Checking code High |
| --- | --- | --- | --- | --- | --- |
| 0x01 | 0x06 | 0x02 | 0x00 0x01 | 0xFC | 0x44 |

Note: the default equipment data 24 hours automatic zero-clearing, power-off will also clear zero.