485 wind direction sensor

user's Guide

JXBS-3001-FX

Ver1.0

# Chapter 1 Product Introduction

## product description

The JXBS-3001-FS series wind direction sensor is small and light, easy to carry and assemble. The three-cup design concept can effectively obtain external environmental information. The shell is made of high-quality aluminum alloy profiles, and the exterior is electroplated and sprayed, which has good anti-corrosion, Anti-corrosion and other characteristics can ensure that the instrument is free from rusting in long-term use, and at the same time, with the smooth internal bearing system to ensure the accuracy of information collection. It is widely used in wind direction measurement in greenhouses, environmental protection, weather stations, ships, docks, and breeding.

## Main parameters

| parameter | Technical index |
| --- | --- |
| Wind direction measurement range | 16positions |
| Wind direction measurement accuracy | 1positions |
| Response time | Less than 5 seconds |
| Baud rate | 9600 |
| Communication port | RS485 |
| Power supply | 12V-24V DC |
| Power | <1W |
| Operating temperature | -30-80℃ |
| Working humidity environment | 0-100%RH（15-95%RH） |

## System framework diagram

# Chapter 2 Hardware Connection

## 2.1Inspection before equipment installation

Please check the equipment list before installing the equipment:

| name | Quantity |
| --- | --- |
| High precision sensor | 1set |
| Wind direction 485 line | 1 piece |
| 12V waterproof power supply | 1set（Optional） |
| USB to 485 device | 1set（Optional） |
| Warranty card/certificate | 1 serving |

### 2.1.1Wiring mode

|  | Thread color | Description |
| --- | --- | --- |
| power supply | brown | Power is positive |
|  | black | Power negative |
| Communication | yellow | 485A |
|  | blue | 485B |

The factory default provides 0.6 meters long wire, customers can extend the wire as needed or wire in order.

## 2.2Installation method

Flange installation is adopted, and the threaded flange connection makes the lower pipe fitting of the wind direction sensor firmly fixed on the flange plate. Four mounting holes of Φ6mm are opened on the circumference of the chassis, and bolts are used to tightly fix it on the bracket to make the whole instrument Keep it at the best level to ensure the accuracy of the wind direction data. The flange connection is convenient to use and can withstand greater pressure.

2.2.1 a fixed way

Chapter 3 Communication Protocol

## 3.1Basic communication parameters

| parameter | content |
| --- | --- |
| coding | 8-bit binary |
| Data bit | 8-bit |
| Parity bit | 无 |
| Stop bit | 1-bit |
| Wrong calibration | CRC lengthy cyclic code |
| Baud rate | 2400bps/4800bps/9600 bps can be set, the factory default is 9600bps |
| coding | 8-bit binary |

## 3.2Data frame format definition

Adopt Modbus-RTU communication protocol, the format is as follows:

Initial structure >= 4 byte time

Address code = 1 byte

Function code = 1 byte

Data area = N bytes

Error check = 16-bit CRC code

End structure >= 4 bytes time

Address code: the address of the transmitter, which is unique in the communication network (factory default 0x01).

Function code: The command function prompt issued by the host, this transmitter only uses function code 0x03 (read memory data).

Data area: The data area is the specific query data area, pay attention to the 16bits data high byte first

CRC code: two-byte check code.

Interrogation frame

| address code | function code | Register address | Register length | Check code low bit | Check code high |
| --- | --- | --- | --- | --- | --- |
| 1byte | 1byte | 2byte | 2byte | 1byte | 1byte |
| Reply frameaddress code | function code | Effective bytes | Data area | Second data area | Nth data area |
| 1byte | 1byte | 1byte | 2byte | 2byte | 2byte |

## Register address

| Register address | PLC configuration address | content | operating |
| --- | --- | --- | --- |
| 0017H | 40018 | Wind direction (unit 1 direction) | Read only |
| 0100H | 40101 | Device address (0-252) | Read and write |
| 0101H | 40102 | Baud rate (2400/4800/9600) | Read and write |

## 3.3Communication protocol example and explanation

### 3.3.1Read the wind direction value of the device address 0x01

Interrogation frame

| address code | function code | initial address | Data length | Check code low bit | Check code high |
| --- | --- | --- | --- | --- | --- |
| 0x02 | 0x03 | 0x00,0x17 | 0x00,0x01 | 0x34 | 0x0E |

Reply frame (for example, read the wind direction value is 3)

| address code | function code | Effective bytes | Wind direction value | Check code low bit | Check code high |
| --- | --- | --- | --- | --- | --- |
| 0x02 | 0x03 | 0x02 | 0x00 0x03 | 0xF8 | 0x45 |

Wind direction:

0003 H (hexadecimal) = 3 => wind direction = true east

### 3.3.2The output value of the wind direction sensor corresponds to the position of the wind direction

0x000ERS485 output data definition

True north: 0x000F    North-northeast: 0x0000

Northeast: 0x0001     East Northeast: 0x0002

True east: 0x0003     East southeast: 0x0004

Southeast: 0x0005     South by Southeast: 0x0006

True South: 0x0007    South by Southwest: 0x0008

Southwest: 0x0009    West Southwest: 0x000A

West: 0x000B        West to Northwest: 0x000C

Northwest: 0x000D    Northwest: 0x000E

## 3.4Notes

Please check whether the packaging is intact, and check whether the transmitter model and specifications are consistent with the product you purchased; if you have any questions, please contact our company as soon as possible.

Please confirm before use: whether the output voltage of the power supply is correct; the positive and negative connections of the power supply and the positive and negative connections of the product; and read the product manual or consult our company. Any error in the wiring will cause irreversible damage to the transmitter.

3.2	Warranty and after-sales

The warranty clauses follow the sensor after-sales clauses of Weihai Jingxun Changtong Electronic Technology Co., Ltd., two years for the sensor host circuit part, one year for gas-sensitive probes, and three months for accessories (housing/plugs/cables, etc.)