Instructions for use of soil water potential transmitter

JXBS-3001-SWP

Ver1.0

# Chapter 1 Product Introduction

## Product overview

The soil water potential sensor is a sensor independently developed by our company that can measure the change of soil moisture at any point in the soil. It is also a sensor based on the principle of dielectric constant; it can quickly, accurately, and accurately measure the soil moisture in different soil layers. Comprehensive monitoring. Soil moisture plays a very important role in the growth of crops. The soil water potential sensor developed by our company can accurately detect the changes in soil moisture, and improve the soil through the detected data, so that the crops are in the best living environment, thereby increasing yield , And greatly facilitate the customer's systematic assessment of soil conditions.

## Application environment

It is widely used in the monitoring of various environmental humidity such as garden irrigation monitoring, moisture monitoring, farming guidance, water conservancy construction, mine monitoring, geological prospecting, scientific experiment and pasture planting.

## Product features

- Real-time monitoring of soil moisture at different levels 

- Move up and down in the plastic pipe to realize the dynamic observation of the soil moisture content of each soil layer

- The equipment adopts standard modbus protocol

## Product advantages

- Using highly sensitive probes, fast response

- Stable, reliable, accurate measurement 

- Small zero drift and good repeatability 

- Product protection grade IP67 

- The product has passed various environmental tests and has anti-interference ability

## Product parameters

| parameter name | Parameter content |
| --- | --- |
| Water potential measurement range | 0～-100kPa |
| measurement accuracy | ±0.1%F.s |
| Resolution | 0.1kPa |
| communication method | RS485 |
| Protection level | IP67 |
| Operating temperature | 5℃-45℃ |
| Working humidity | 0 to 95% (relative humidity), no condensation |
| DC power supply (default) | 12-24V DC |
| Power consumption | ≤0.5W（@12V DC , 25℃） |
| output signal | RS485 output (Mondbus protocol) |
| Working pressure range | 0.9-1.1atm |

# Chapter 2 Hardware Connection

## 2.1Product appearance

The following two pictures are the external dimensions of the 485 version, as shown in the figure:

## 2.2Product list

Please check the equipment list before installing the equipment

| name | Quantity |
| --- | --- |
| High precision sensor | 1 set |
| 12V waterproof power supply | 1 set (optional) |
| USB to 485 device | 1 set (optional) |
| Warranty card/certificate | 1份 |

## 2.3Wiring instructions

The equipment power supply adopts 12V DC power supply. When wiring the 485 signal line, pay attention to the two wires A and B not to be reversed, as shown in the figure (table):

|  | Thread color | Description |
| --- | --- | --- |
| power supply | brown | Power is positive（12-24V DC） |
|  | black | Power negative |
| Communication | Yellow (gray) color | 485-A |
|  | blue | 485-B |

The factory default provides 1.25 meters long wire, customers can extend the wire as needed or wire in order. Note that there is no yellow line in the line sequence that may be provided in some factory batches. At this time, the gray line is equivalent to replace the yellow line.

## 2.4 Use matters

(1) When using and installing the soil water potential sensor, the two links of using airless water and removing the air in the clay pipe are mainly mastered. The air in the degas cylinder not only affects the measurement accuracy of the instrument and causes delays, but also seriously affects the normal use of the instrument.

(2) Inject airless water (cold boiled water) into the water potential sensor until it is full, stand the sensor upright for 10-20 minutes (without a lid), let the water wet the clay tube, and see water drip from the surface of the clay tube. Then fill the sensor with airless water, seal it with a lid, and put the instrument upright to let the clay tube evaporate in the air. About two hours later, at this time, there will be buried bubbles escaping from the clay tube, piezoelectric sensor, and plexiglass tube. Tap the sensor gently to concentrate the bubbles on the upper part. Then immerse the clay tube in the airless water. At this time, the transmitter reads back to near zero. Open the lid, refill with airless water, add the cover to seal, and put the instrument upright to let the clay tube evaporate in the air. The above operation is repeated 2-3 times. Repeat the degassing process several times. While degassing, the air in the sensor is automatically discharged and filled with water.

(3) The instrument is used in wet soil to measure the process from wet to dry, and the water potential sensor can start to measure when it is saturated; if it needs to be used in the dry soil, measure the process from dry to wet, the initial content of the dry soil The amount of water must be within the measuring range of the water potential sensor (<0.85 bar). The water potential sensor must be air-dried to reach the suction value of the measured dry soil, and then inserted into the soil for use.

(4) When used outdoors, due to large temperature changes and long service cycles, it is necessary to take some protective measures for the water potential sensor and transmitter. For example, cover the water potential sensor to avoid sunlight trend. In order to reduce temperature fluctuations on the sensor If affected, the sensor can be buried in the soil. In order to prevent the infiltration of moisture in the soil, a plastic tube sealing sleeve is made to protect the sensor.

(5) Generally speaking, if the air inside the sensor is basically removed before burying, and the soil humidity is within the measuring range of the sensor, it can be maintained continuously for 20-25 days without adding water. When the temperature drops to freezing point, the sensor should be evacuated.

(6) The clay head should not be oily to avoid clogging the pores and the sensor failure.

(7) The instrument is usually used in the temperature range of 5~45℃. At the same time, attention should be paid to avoid interference from other electromagnetic fields.

## 2.5Measuring method

Select a suitable measurement location, measure the depth according to the need, and carry out the punch test according to the size, fill the pit tightly, and the measuring instrument starts to work. After a period of stability, it can be carried out for several days, months or even longer. Time measurement and recording. The collection method is shown in the figure:

## 2.6Notes

- The measuring instrument must be inserted vertically into the test environment

- When the equipment is buried in the test environment, do not press too hard 

- Not suitable for absolute moisture measurement of saline-alkali soil, sandy soil, or other powdery objects with high salt content 

- Do not use in environments where soil impurities, stones, roots, and hardly dissolve

# Chapter 3 Communication Protocol

## 3.1Basic communication parameters

| parameter | content |
| --- | --- |
| coding | 8-bit binary |
| Data bit | 8-bit |
| Parity bit | No |
| Stop bit | 1-bit |
| Error checking | CRC (Redundant Cyclic Code) |
| Baud rate | 2400bps/4800bps/9600bps can be set, the factory default is 9600bps |

## 3.2Data frame format definition

Using Modbus-RTU communication protocol, the format is as follows: Time of initial structure ≥ 4 bytes Address code = 1 byte Function code = 1 byte Data area = N bytes Error check = 16-bit CRC code Time to end structure ≥ 4 bytes Address code: The address of the transmitter, which is unique in the communication network (factory default 0x01). Function code: The command function instruction issued by the host, this transmitter only uses function code 0x03 (read register data). Data area: The data area is the specific communication data, pay attention to the high byte of 16bits data first! CRC code: two-byte check code.

Interrogation frame

| address code | function code | Register start address | Register length | Check code low bit | Check code high |
| --- | --- | --- | --- | --- | --- |
| 1 byte | 1 byte | 2 byte | 2 byte | 1 byte | 1 byte |

Reply frame

| address code | function code | Effective bytes | Data area | Second data area | Nth data area | Check code |
| --- | --- | --- | --- | --- | --- | --- |
| 1 byte | 1 byte | 1 byte | 2 byte | 2 byte | 2 byte | 2 byte |

## 3.3Register address

| Register address | PLC or configuration address | content | operating |
| --- | --- | --- | --- |
| 0002H | 40003 | Soil water potential value (unit: 0.1kPa) | Read only |
| 0100H | 40101 | Device address (0-252) | Read and write |
| 0101H | 40102 | Baud rate (2400/4800/9600) | Read and write |

## 3.4 Communication protocol example and explanation

### 3.4.1 Read the soil water potential value of the device address 0x01

Interrogation frame

| address code | function code | starting address | Data length | Check code low bit | Check code high |
| --- | --- | --- | --- | --- | --- |
| 0x01 | 0x03 | 0x00 0x02 | 0x00 0x01 | 0x25 | 0xCA |

Reply frame

| address code | function code | Effective words | Water potential | Check code Low | Check code High position |
| --- | --- | --- | --- | --- | --- |
| 0x01 | 0x03 | 0x02 | 0x02 0x92 | 0x5A | 0x3D |

Soil water potential: 0292H (hexadecimal) = 658 => soil water potential = 65.8kPa